## Creation of the Cantilver Beam used in the Dynamic Analysis Tutorials

This file describes the GUI (Graphic User Interface) steps to create the following cantilever beam in ANSYS.

- Open preprocessor menu

- Give example a Title

Utility Menu > File > Change Title ...

- Give example a Jobname

Utility Menu > File > Change Jobname ...

Enter 'Dynamic' for the jobname

- Create Keypoints

Preprocessor > Modeling > Create > Keypoints > In Active CS

We are going to define 2 keypoints (the beam vertices) for this structure as given in the following table:

| Keypoint | Coordinates (x,y) |
| --- | --- |
| 1 | (0,0) |
| 2 | (1,0) |

- Define Lines

Preprocessor > Modeling > Create > Lines > Lines > Straight Line

Create a line between Keypoint 1 and Keypoint 2.

- Define Element Types

Preprocessor > Element Type > Add/Edit/Delete...

For this problem we will use the BEAM3 (Beam 2D elastic) element. This element has 3 degrees of freedom (translation along the X and Y axis's, and rotation about the Z axis). With only 3 degrees of freedom, the BEAM3 element can only be used in 2D analysis.

- Define Real Constants

Preprocessor > Real Constants... > Add...

In the 'Real Constants for BEAM3' window, enter the following geometric properties:

  - Cross-sectional area AREA: 0.0001

  - Area Moment of Inertia IZZ: 8.33e-10

  - Total beam height HEIGHT: 0.01

This defines an element with a solid rectangular cross section 0.01 m x 0.01 m.

- Define Element Material Properties

Preprocessor > Material Props > Material Models > Structural > Linear > Elastic > Isotropic

In the window that appears, enter the following geometric properties for steel:

  - Young's modulus EX: 2.068e11

  - Poisson's Ratio PRXY: 0.3

To enter the density of the material, double click on 'Linear' followed by 'Density' in the 'Define Material Model Behavior' Window

Enter a density of 7830

Note: For dynamic analysis, both the stiffness and the material density have to be specified.

- Define Mesh Size

Preprocessor > Meshing > Size Cntrls > ManualSize > Lines > All Lines...

For this example we will specify 10 element divisions along the line.

- Mesh the frame

Preprocessor > Meshing > Mesh > Lines > click 'Pick All'